## Slide 1
BIG DATA · INDUSTRIAL IoT · SPARK ML
Real-Time Railway
Compressor
Monitoring
A containerized streaming pipeline with Spark MLlib anomaly detection and Superset dashboards.
Kafka
Spark
MLlib K-Means
Superset
LIVE · TP3 PRESSURE STREAM
threshold 3.03
ANOMALY DETECTED
MetroPT-3 sensor stream → insight
PROJECT TEAM
Felopater Adel
Abubaker Kamel
Ahmed Salah Heusien
Donya Samy Qurani
Omar Mohamed Kenawi
Ahmed Abdelreman
Notes: Introduce the project: a real-time big data pipeline that watches railway air-compressor sensors and flags abnormal behavior before it becomes a failure.

## Slide 2
THE PROBLEM
Why this proposal matters
MetroPT · Railway Compressor Monitoring
02 / 10
Storing sensor data is easy.
Turning it into maintenance signals before failures get expensive is the real challenge.
Continuous sensor events
Readings arrive every few seconds, nonstop.
Operational pressure changes
Manual checks are slow and miss early signs.
Hidden abnormal behavior
Only streaming can watch every single reading.
PROPOSAL PURPOSE
Build an end-to-end big data pipeline that detects unusual compressor behavior and presents it clearly to decision makers.
Notes: The value is not storage — it is early warning. Walk through the three pain points, then land on the purpose.

## Slide 3
DATA SOURCE
MetroPT-3 industrial IoT dataset
MetroPT · Railway Compressor Monitoring
03 / 10
1.5M+
sensor records
15
sensor features
2020
time range
SENSOR GROUPS
Pressure
TP2 · TP3 · Reservoirs
Temperature
Oil temperature
Electrical
Motor current
Why it fits
Time-series behavior matches streaming windows
Real compressor operation, not synthetic data
Works for anomaly detection without labels
Can be replayed at controlled speeds
Notes: MetroPT-3 is real railway compressor telemetry: 1.5M+ rows, 15 signals. It replays naturally as a stream and needs no labels for K-Means.

## Slide 4
ARCHITECTURE
Proposed system architecture
MetroPT · Railway Compressor Monitoring
04 / 10
01
DATA SOURCE
MetroPT-3
CSV replayed as a live stream
02
INGESTION
Kafka
Buffers events in a topic
03
PROCESSING
Spark
Structured Streaming, windowed KPIs
04
STORAGE
PostgreSQL
KPIs + AI predictions
05
INSIGHTS
Superset
Dashboards for decisions
features
predictions
AI layer · Spark MLlib K-Means
Learns normal behavior, scores each event
One stack, end to end:
stream → model → store → visualize
Apache Airflow orchestration & health checks
Docker Compose portable, one-command setup
Notes: Follow the data left to right: CSV replay → Kafka → Spark Streaming → PostgreSQL → Superset. Spark hands features to K-Means; predictions land in PostgreSQL. Airflow and Docker wrap the whole stack.

## Slide 5
INGESTION LAYER
Streaming ingestion with Kafka
MetroPT · Railway Compressor Monitoring
05 / 10
Kafka decouples data generation from processing, so Spark consumes the sensor stream reliably.
MetroPT-3 CSV
Replay producer
Kafka topic
Spark consumer
Each sensor row becomes one JSON event
Topic partitions allow parallel consumption
Adjustable event rate for demos and stress tests
Kafka can be verified live from the terminal
Notes: Each CSV row is published as a JSON event. The producer sets the pace, the topic buffers, Spark subscribes.

## Slide 6
PROCESSING LAYER
Distributed processing with Spark
MetroPT · Railway Compressor Monitoring
06 / 10
1
Parse JSON events
Decode every Kafka message into sensor columns
2
Clean sensor types
Cast readings to numbers, drop broken rows
3
Window aggregations
Compute KPIs over 60-second windows
4
Store KPIs
Write each micro-batch to PostgreSQL
2
WORKERS
distributed execution
60s
WINDOW
streaming window
5s
TRIGGER
micro-batch interval
KPI OUTPUT · spark_kpis
window_start timestamp
event_count int
avg_tp3 double
avg_motor_current double
batch_duration ms
Notes: Spark Structured Streaming reads Kafka continuously: parse, clean, aggregate per 60-second window, write KPIs every 5-second trigger.

## Slide 7
AI LAYER
Anomaly detection with Spark MLlib K-Means
MetroPT · Railway Compressor Monitoring
07 / 10
Training data
Feature scaling
K-Means clusters
Anomaly score
HOW IT SEES THE DATA (illustrative)
distance to nearest centroid → score → Normal / Anomaly
303,959
training rows
K = 5
clusters
3.032087
anomaly threshold
577
anomalies found
Notes: Unsupervised: K-Means learns 5 clusters of normal operation. Records far from every centroid (score above 3.03) are flagged — 577 anomalies out of ~304K training rows.

## Slide 8
STORAGE & ANALYTICS
From tables to business insight
MetroPT · Railway Compressor Monitoring
08 / 10
spark_kpis
Windowed KPIs per micro-batch
anomaly_predictions
Score + Normal / Anomaly label
Superset dashboard
Trends and spikes, instructor-friendly
Compressor anomalies over time
ILLUSTRATIVE
Chart: 
| 08:00 | 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00 | 16:00 | 17:00 | 18:00 | 19:00
Anomalies | 3 | 4 | 2 | 5 | 4 | 6 | 21 | 34 | 9 | 4 | 3 | 4
Spike = maintenance signal
Superset turns the anomaly spike into a business insight — not just terminal output.
Notes: PostgreSQL holds KPIs and predictions; Superset makes the spike obvious to non-technical viewers.

## Slide 9
OPERATIONS
Orchestration & reproducibility
MetroPT · Railway Compressor Monitoring
09 / 10
Docker Compose
One command starts Kafka, Spark, PostgreSQL, Superset and Airflow.
Airflow DAG
Health checks confirm every service is ready before the demo.
Repeatable demo
Same pipeline, same results — from a clean start, every time.
AIRFLOW SCOPE
Health checks for PostgreSQL, Kafka and Spark — the pipeline is verified ready before the demo starts.
Every component starts from scratch
Model files are saved and reused after restart
No cloud dependency for the local demo
Dashboards persist through Docker volumes
Notes: Reproducibility is a feature: anyone can clone the repo, run docker compose up, and get the same demo.

## Slide 10
DEMO STORY & OUTCOMES
From raw sensors to decisions — live
01
Start stack
02
Replay data
03
Process stream
04
Show AI
05
Dashboard
EXPECTED VALUE
Real-time ingestion, distributed processing, anomaly detection, persistent storage and visual decision support — in one reproducible platform.
“The system converts raw MetroPT sensor data into actionable compressor health insights.”
MetroPT · Railway Compressor Monitoring
10 / 10
Notes: Walk the live demo in five beats, then close with the one-line takeaway.

## Slide 11
LIVE · Q&A SESSION
Thank you
Any questions?
From raw MetroPT sensor data to actionable compressor health insights.
?
MetroPT · Railway Compressor Monitoring